## Slide 1: A5_23 Diffuser wire visual appearance at top ends
Before
After
Due to transparent after Assy LED wire visual at top ends
Modified diffuser through shaded at both edges ,prevent from visual appearance

## Slide 2: A5_23Speaker rattling sound
Before
After
Speaker bracket rattling sound issue
Modified speaker bracket implement issue resolved permanently

## Slide 3: A5_23 Window lens vinyl film implementation
Before
After
LCD main lens causes scratch issue
Praposed and developed the main lens vinyl film avoided such issue
Anuj

## Slide 4: A5_23 laser string location
Before
After
Laser string location are near by test point creates issue
String location updated into layout as well PCB avoided issue
Anuj

## Slide 5: A5_23A-sheel hard fitment issue
Before
After
A-shell create hard fitment issue
Provided chamfer at highlighted position ,verified by PD ,SQA no hard issue observed
Anuj